# Fake rock recipe

# As told by Leonard, 16 march 2004

(There is a binder in Leonard’s office on the top shelf towards the left with more documentation.)

- Calculate the volume of fake rock needed.

- Take that volume and double or triple it.

- Using density, calculate the masses of sand and cement needed.  The sand is white, 100 micron, Oklahoma (?) pure silica sand, there should be a few bags left in 277. The cement is standard Portland cement. For debris flow experiments, 1:10 cement : sand is recommended as a starting point (relatively weak).

- Weigh the sand and put it in the tub (black cement mixing tub).

- Weigh the cement.  Since the cement is hard to mix, since it is so fine, sprinkle it gently (using a dust mask) evenly over the surface of the sand, and then mix (with the “holed hoe”).  You may even want to split the cement into several parts to do this.

- Using the hoe, mix until homogeneous, there should be no more clumps or pockets of bright white sand. Mix, mix, mix.

- Now comes the water. You may look to the documentation to get an idea of how much water will be needed, but it will be a trial and error procedure. Keep track of the water for future reference.  Most water goes towards coating the particles, a very small amount of water will reach and exceed the liquid limit (loosely defined) quickly. You ideally want the mixture at the threshold of flowing, so that it will support a 45 degree angle but will still flow when you agitate it.

- Keep mixing and mixing.

- Pour the cement into moistened forms. (You don’t want the liquid to seep out to moisten the form.)  There are wooden forms screwed together or you can use paper (carton-like) disposable forms (paint buckets, for example, or milk cartons).  However, there is a lower limit to how thin cement may be poured before it loses strength.   Also, for the strength tests, 2 by 2 inch cylinder cores are needed.

- You must tap on the cement to help it set, and get the air and water bubbles to come to the surface.  For wooden forms, use a hammer to tap directly on the wood.  For paper forms, put them on a plank and tap the plank.  Water should pool at the top, which is fine.

- The cement should be cured for 21 days to reach 90% (or some large value like that) of its strength. Be consistent curing them wet or dry (see Sklar Geology paper for more details).

- After this, the cement can be cut on the rock saws for erosion experiments. Cut off the edges, which may be incompetent.